## Slide 1
WIRELESS COMMUNICATIONS
Base Station Subsystem (BSS) Architecture
Co-Channel Interference (CCI) | Adjacent-Channel Interference (ACI)
Presented by
D V Sai Kumar
Register Number: 192372321
GSM NETWORKS • RADIO RESOURCE MANAGEMENT

## Slide 2
Introduction
OVERVIEW
02
The Base Station Subsystem (BSS) is the radio-access part of a GSM network. It connects mobile devices to the core network through radio communication.
Connects users
Carries voice and data between mobile stations and the network.
Manages radio links
Assigns radio channels and supports handover as users move.
Needs clean spectrum
Interference can reduce call quality, coverage and capacity.
Presentation focus
BSS architecture → CCI → ACI → Comparison and mitigation
D V Sai Kumar • 192372321
02

## Slide 3
BSS Architecture
COMPONENTS
03
Mobile Station
Phone / SIM
BTS
Radio transmitter and receiver
BSC
Controls multiple BTSs
Core Network
MSC and other systems
Radio link
Abis
A interface
BTS — Base Transceiver Station
• Sends and receives radio signals • Provides coverage for a cell • Handles the radio interface
BSC — Base Station Controller
• Controls a group of BTSs • Allocates radio channels • Supports handover and power control
TRAU — Transcoding / Rate Adaptation
Adapts speech coding and data rates where used. Its location can vary by implementation.
Note: The MSC is part of the core network, not the BSS. TRAU placement may vary.
D V Sai Kumar • 192372321
03

## Slide 4
Co-Channel Interference (CCI)
INTERFERENCE
04
Definition
Interference between signals transmitted on the same frequency by different cells.
Cell A f1
Cell B f2
Cell C f1
Same frequency f1
Causes & effects
• Frequency reuse too close together • Strong neighboring-cell signals • Lower signal quality / more errors
Mitigation: careful frequency reuse planning, power control, antenna optimization and sectorization.
D V Sai Kumar • 192372321
04

## Slide 5
Adjacent-Channel Interference (ACI)
INTERFERENCE
05
Definition
Interference from a nearby frequency channel that affects the desired receiver channel.
Channel N−1
Desired Channel N
Channel N+1
Frequency →
Causes & effects
• Poor filtering or receiver selectivity • Insufficient channel separation • Distortion, bit errors or reduced sensitivity
Mitigation: better RF filters, appropriate channel spacing, careful channel assignment and power control.
D V Sai Kumar • 192372321
05

## Slide 6
CCI vs ACI: Comparison
SUMMARY
06
Feature
CCI
ACI
Frequency used
Same frequency
Nearby / adjacent frequencies
Typical cause
Frequency reuse between cells
Imperfect filtering or receiver selectivity
Main impact
Co-channel signal competes with desired signal
Energy from a neighboring channel affects reception
Main solutions
Frequency planning, cell separation, antenna/power control
RF filters, channel assignment, channel spacing
Example
Two cells transmit on f1
A strong signal on channel N+1 affects channel N
Both degrade radio performance, but the interference source and best mitigation method differ.
D V Sai Kumar • 192372321
06

## Slide 7
Conclusion
KEY TAKEAWAYS
07
BSS
Provides the radio connection between mobile stations and the core network.
CCI
Same-frequency interference is managed mainly through frequency reuse planning and cell design.
ACI
Adjacent-channel interference is reduced through filtering, channel planning and power control.
Effective interference management improves:
Call quality
Network reliability
Spectrum efficiency
Thank You
D V Sai Kumar | Register Number: 192372321

## Slide 8
Questions & References
DISCUSSION
08
Thank you for your attention.
Questions?
Key terms
BSS — Base Station Subsystem BTS — Base Transceiver Station BSC — Base Station Controller CCI — Co-Channel Interference ACI — Adjacent-Channel Interference
Suggested references
• 3GPP GSM/GERAN technical specifications • ITU-R recommendations on radio-frequency management • Standard GSM / mobile communications textbooks
Presented by D V Sai Kumar • 192372321
D V Sai Kumar • 192372321
08